## Slide 1: SONATA: Query-Driven Network Telemetry
Arpit Gupta
Princeton University
Rob Harrison, Ankita Pawar, Marco Canini,
Nick Feamster, Jennifer Rexford, Walter Willinger

## Slide 2
Existing Telemetry Systems
Compute
Store
Queries
Packet Capture
Collection
Analysis
NetFlow
SNMP

## Slide 3
Existing Telemetry Systems
Compute
Store
Collection
Analysis
Existing Systems are Query-Agnostic!
Queries

## Slide 4: Problems with Status Quo
Expressiveness
  Configure collection & analysis stages separately
  Static (and often coarse) data collection
  Brittle analysis setup---specific to collection tools
Scalability
  Hard to scale query execution as:
    Traffic Volume increases and/or
    Number of Queries increases
Network Telemetry Systems should be Expressive & Scalable

## Slide 5: Idea 1: Declarative Query Interface
Extensible Packet-As-Tuple Abstraction
  Treat packets as tuples carrying header, payload, and meta fields
Expressive Dataflow Operators
  Most telemetry applications
    Collect aggr. statistics over subset of traffic
    Join results of one analysis with the other
  Express them as declarative queries composed of dataflow operators, e.g. map, reduce, filter, join etc.
Notes:   , e.g., timestamp, queue length etc.

## Slide 6: Example Queries
Detecting Newly Opened TCP Connections
Detect hosts for which the number of newly opened TCP connections exceeds threshold (Th)
victimIPs = pktStream
      .filter(p => p.tcp.flag == SYN)
      .map(p => (p.dstIP, 1))
      .reduce(keys=(dstIP,), sum)
      .filter((dstIP, count) => count > Th)
      .map((dstIP, count) => dstIP)
Collect aggr. stats over subset of traffic

## Slide 7: Example Queries
Detecting Traffic Anomalies
Detect hosts for which the number of unique source IPs sending DNS response messages exceeds threshold (Th)
pvictimIPs = pktStream
      .filter(p => p.udp.sport == 53)
      .map(p => (p.dstIP, p.srcIP))
      .distinct()
      .map((dstIP, srcIP) => (dstIP, 1))
      .reduce(keys=(dstIP,), sum)
      .filter((dstIP, count) => count > Th)
      .map((dstIP, count) => dstIP)
Apply multiple aggregations over the packet tuple streams

## Slide 8: Example Queries
Confirming Reflection Attacks
Detect hosts with traffic anomalies that are of type RRSIG
victimIPs = pktStream
    .filter(p => p.udp.sport == 53)
    .join(pVictimIPs, key=‘dstIP’)
    .filter(p => p.dns.rr.type == RRSIG)
    .map(p => (p.dstIP, 1))
    .reduce(keys=(dstIP,), sum)
    .filter((dstIP, count) => count > T2)
    .map((dstIP, count) => dstIP)
Join results of one analysis with the other

## Slide 9: Changing Status Quo
Expressiveness
  Express dataflow queries over packet tuples
  Not tied to low-level (3rd party/platform-specific) APIs
  Trivial to add new queries and change collection tools
Easier to express network telemetry tasks!

## Slide 10
Query Execution
Use Scalable Stream Processors
Packet Capture
Stream Processor
Queries
Packet Tuples
Process all (or subset of) captured packet tuples using state-of-the-art Stream Processor
Expressive but not Scalable!

## Slide 11: Idea 2: Query Partitioning
Observation
  Data plane can process packets at line rate
How it works?
  Execute subset of dataflow operators in the data plane
Trade-off
  Trades workload at stream processor at the cost of additional resource usage in the data plane

## Slide 12
Query Partitioning in Action
Programmable Data Plane
Data Plane
Configurations
Stream Processor
Runtime
Queries
Partition Queries b/w
Switches and Stream Processor
Packet Tuples

## Slide 13: Query Partitioning in Action
pktStream
.filter(p=>p.srcPort==53)
.map(p=>(p.dstIP,p.srcIP))
.distinct()
.map((dstIP, srcIP)=>(dstIP,1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP,count)=>count>Th)
.map((dstIP, count) => dstIP)
Stream Processor
Traffic Anomaly Query
Programmable Data Plane
pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
.map((dstIP, count) => dstIP)

## Slide 14: Compiling Queries for PISA Targets
Pktin
Pktout
Register
M | A
M | A
M | A
M | A
pktStream
.filter(p=>p.udp.sport==53)
.map(p=>(p.dstIP,p.srcIP))
.distinct()
PISA Target
Monitoring Port
See Tutorial 2 for details

## Slide 15: Limited Data-Plane Resources
Pktin
Pktout
Register
M | A
M | A
M | A
M | A
Physical Stages
Number of Physical Stages
Number of Actions per Stage

## Slide 16: Limited Data-Plane Resources
Pktin
Pktout
Register
M | A
M | A
M | A
M | A
Available Memory per Stage
SRAM for Stateful Operations

## Slide 17: Limited Data-Plane Resources
Pktin
Pktout
Register
M | A
M | A
M | A
M | A
Available State for Metadata fields
Packet Header Vector

## Slide 18: Selecting Query (Partitioning) Plans
Given:
  Queries & Training Data
Objective:
  Minimize the workload at Stream Processor
Constraints:
  Available memory per stage
  Available space for metadata fields
  Number of actions per stage
  Total number of stages
Solve Query Planning Problem as an ILP

## Slide 19: Idea 3: Iterative Refinement
Observation
  Tiny fraction of traffic or flows satisfy telemetry queries
How it works?
  Execute queries at coarser levels
  Iteratively zoom-in on interesting traffic over time
Trade-offs
  Trades workload at stream processor at the cost of additional detection delay

## Slide 20
Iterative Refinement in Action
Programmable Data Plane
Data Plane
Configurations
Stream Processor
Runtime
Packet Tuples
Iterative Refinement
Queries’ Output Drives further Processing
Queries

## Slide 21: Iterative Refinement in Action
Q8(W) = pktStream
.filter(p=>p.udp.sport==53)
.map(dstIP=>dstIP/8)
.map(p=>(p.dstIP,p.srcIP))
…
Q16(W+1) = pktStream
.filter(p=>p.udp.sport==53)
.filter(p=>p.dstIP/8 in Q8(W))
.map(dstIP=>dstIP/16)
.map(p=>(p.dstIP,p.srcIP))
…
Time
W
W + 1
Traffic Anomaly Query
/8
Query-Driven Network Telemetry!
pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
.map((dstIP, count) => dstIP)
 /16
Refinement Key = dstIP

## Slide 22: Quantify Performance Gains
Realistic Workload
  Anonymized packet traces from a large ISP
  Processing 20 M packets per second (~100 Gbps)
Typical Telemetry Tasks
  New TCP, SSH Brute, Super Spreader, Port Scan, DDoS, SYN Flood, Completed Flows, Slow Loris, …
Comparisons
  All-SP, Filter-DP, Max-DP, Fix-REF

## Slide 23: Single-Query Performance
Reduces workload at stream processor by up to seven orders of magnitude

## Slide 24: Multi-Query Performance
Reduces workload at stream processor by up to three orders of magnitude

## Slide 25: Sensitivity Analysis Data-Plane Resources
Sonata makes the best use of available limited data-plane resources

## Slide 26: Changing Status Quo
Expressiveness
  Express Dataflow queries over packet tuples
  Not worry about how and where the query is executed
  Adding new queries and collection tools is trivial
Scalability
  Answers multiple queries for traffic volume as high as 100 Gb/s in real-time
Sonata is Expressive & Scalable!

## Slide 27: Sonata Implementation
Streaming Driver
Programmable Data Plane
Packets In
Stream Processor
Query Interface
Queries
Q1
Output
Tuples
Q2
QN
Queries
Core
Data Plane Driver
Packets Out
Query Partitioning
Iterative Refinement
Notes: Single switch setup

## Slide 28: AT&T Use Cases

## Slide 29: Performance Monitoring
Monitor various performance metrics
TCP-Monitoring =
pktStream
.map(p => (key, perf-metric))
nBytes,
loss,
latency,
…
5-tuples,
ingress-egress pairs,
src-dst pairs,
..

## Slide 30: Performance Monitoring
Identify flows for which the traffic volume exceeds threshold (T)
Heavy-Hitters =
pktStream
.map(p => (p.5-tuple,p.nBytes))
.reduce(keys=(5-tuple,), sum)
.filter((5-tuple,bytes) => bytes > T)
.map((5-tuple,bytes)=> 5-tuple)
Use Sonata for Collection & Analysis

## Slide 31: Detecting Microbursts
Detect ports for which the total traffic volume exceeds a threshold (T1)
mBursts = pktStream
      .map(p => (p.port, p.nBytes))
      .reduce(keys=(port,), sum)
      .filter((port, bytes) => bytes > T1)
      .map((port, bytes) => port)

## Slide 32: Analyzing Microbursts
Analyze which flows contribute to microbursts
Top-Contributors = pktStream
.map(p => (p.port,p.5-tuple,p.nBytes))
.join(mBursts, key=‘port’)
.map((port,5-tuple,nBytes)=>(5-tuple,nBytes))
.reduce(keys=(5-tuples,), sum)
.filter((5-tuples,bytes) => bytes > T2)
.map((5-tuples,bytes) => 5-tuples)

## Slide 33: Future Work

## Slide 34: Extend Packet Tuples
Currently, dns.rr.type is parsed in user-space
Possible to parse it in the data plane itself
Layers of Interest:
  DNS
  SMTP
  …
victimIPs(t) = pktStream(W)
    …
    .filter(p => p.dns.rr.type == RRSIG)
    …

## Slide 35: Extend Dataflow Operators
Extend existing Operators
  Reduce
    Currently, only sum function is supported
    Implement more complex aggregation functions
  Join
    Currently, only inner join is supported
    Implement full outer, Cartesian, left/right inner/outer joins
Add new Operators
  Flat Map
  Sample

## Slide 36: Support Network-Wide Queries
Extend Query Interface
  Support dataflow queries over all packets tuples at any location
  Extract path-related fields, e.g. traversed hops, queue lengths per hop, path latency etc.
Scale Query Execution
  Distribute aggregation operations and thresholds along the path
  Use topological hierarchy for iterative refinement
  Dynamically route packets for processing

## Slide 37: Summary
SONATA enables expressive and scalable network telemetry using
  Declarative Query Interface
  Query Partitioning
  Iterative Refinement
Contribute to Sonata Project
  10+ active members and growing
  GitHub: github.com/Sonata-Princeton/SONATA-DEV
sonata.cs.princeton.edu